## Slide 1
SERVO MOTOR WITH MOTOR DRIVER
01
CSE 315
Peripherals & Interfacing
Durjoy Mistry
UAP CSE,
Year 3 | Semester 2

## Slide 2
02
Servo motor with motor driver
Have you ever wondered?

## Slide 3
Agenda
  Servo Motor Basics
  Servo Motor Basics(Visuals)
  How does it work?
  Types
  Types Explanation
  Working Principles of a DC Servo Motor
  Working Principles of an AC Servo Motor
  Driving Servo Motors with L293D Shield
  Driving Servo Motors with L293D (Video)
  Code
  Code Explanation
  Servo Motor Applications
03

## Slide 4
04
Servo motor with motor driver
Servo Motor Basics
  Control circuit
  Servo motor
  Shaft
  Amplifier
  Encoder or resolver.
Servo motors are part of a closed-loop system and are comprised of several parts namely :

## Slide 5
05
Servo Motor Basics(Visuals)

## Slide 6
06
How Does it work?(Video)
SOURCE
Servo motor with motor driver

## Slide 7
07
Servo motor with motor driver
Types(3 x 2)
  AC or DC
  Brush or Brushless(DC)
  Synchronous or Asynchronous(AC)

## Slide 8
08
Servo motor with motor driver
AC or DC
AC
DC
Point
speed is directly proportional to the supply voltage with a constant load.
speed is determined by the frequency of the applied voltage and the number of magnetic poles.
  Performance
DC motors are also used in servo systems but recommended when there's no demand of high precision.
AC motors will withstand higher current and are more commonly used where high repetitions and high precision are required.
  Usablity

## Slide 9
09
Servo motor with motor driver
Brushed or Brushless(DC)
Brushed
Brushless
Point
Brushless motors are comparatively more expensive and harder to operate
Brushed motors are generally less expensive and simpler to operate
  Cost & Usability
Less reliable,
have lower efficiency,
and are more noisy.
more reliable
have higher efficiency
and are less noisy.
  Performance

## Slide 10
10
Servo motor with motor driver
Synchronous or Asynchronous(AC)
Synchronous
Asynchronous
Point
Asynchronous motor is cheaper compared to synchronous motors.
Synchronous motor is costlier compared to asynchronous motors.
  Cost
Stator speed is not equal to the speed of rotor. Rotor is slower than stator.
Stator speed is equal to the speed of totor
  Speed

## Slide 11
11
Servo motor with motor driver
Working Principles of a DC Servo Motor(1)

## Slide 12
12
Servo motor with motor driver
Working Principles of a DC Servo Motor(2)
SOURCE

## Slide 13
13
Servo motor with motor driver
Working Principles of a DC Servo Motor(Video)
SOURCE

## Slide 14
14
Servo motor with motor driver
Working Principles of a AC Servo Motor(1)
SOURCE

## Slide 15
15
Servo motor with motor driver
Working Principles of a AC Servo Motor(2)
SOURCE

## Slide 16
16
Servo motor with motor driver
Working Principles of a AC Servo Motor(Video)- Synchronous
SOURCE

## Slide 17
17
Servo motor with motor driver
Working Principles of a AC Servo Motor(Video)-Asynchronous
SOURCE

## Slide 18
18
L293D Motor Driver
Servo Terminal
External Power
Supply Terminal
Power
Supply Terminal
Reset
Stepper #2

## Slide 19
19
Driving Servo Motors with L293D Shield
Orange: Signal
Red: VCC
Last: Ground
Ground, VCC, Signal

## Slide 20
Driving Servo Motors with L293D (Video)
20
PLAY THIS ON
See
Codes

## Slide 21
21
Code + Explanation
Servo motor with motor driver
#include <Servo.h> //Servo library
Servo servo_test; //initialize a servo object for the connected servo
int angle = 0;
void setup()
{
servo_test.attach(9); // attach the signal pin of servo to pin9 of arduino
}
When the program starts running, the servo motor will rotate slowly from 0 degrees to 180 degrees, one degree at a time. When the motor has rotated 180 degrees, it will begin to rotate in the other direction until it returns to the home position.

## Slide 22
22
Code + Explanation
Servo motor with motor driver
void loop()
{
for(angle = 0; angle < 180; angle += 1) // command to move from 0 degrees to 180 degrees
{
servo_test.write(angle); //command to rotate the servo to the specified angle
delay(15);
}
delay(1000);
for(angle = 180; angle>=1; angle-=5) // command to move from 180 degrees to 0 degrees
{
servo_test.write(angle); //command to rotate the servo to the specified angle
delay(5);
}
delay(1000);
}

## Slide 23
23
Servo motor with motor driver
Servo Motor Applications

## Slide 24
24
Thank you!
LET US KNOW IF YOU HAVE QUESTIONS OR CLARIFICATIONS.
Servo motor with motor driver

## Slide 25
25
Reference
Servo motor with motor driver
  slide 3-17 (Servo Motor Basics, Type, Working Principles):
https://realpars.com/servo-motor/
  Slide 18-19 (L293D Motor Driver):
https://lastminuteengineers.com/l293d-motor-driver-shield-arduino-tutorial/
  Slide 20 (Connect with Arduino):
https://youtu.be/zZ1sYtoo5gw
  Slide 21-22 (Code):
https://www.allaboutcircuits.com/projects/servo-motor-control-with-an-arduino/